Frequency Divider
 Delta Sigma Modulation-Circuit Implementation
Student: Abhinav S
Advisor: Abhishek Srivastava
May, 2022

---
Project Summary
Project Title	IWR1843BOOST
PI	Dr. Abhishek Srivastava
Research lab	IC~WiBES / Integrated Circuits inspired by Wireless and Biomedical Electronic Systems
Research center	Center for VLSI and Embedded System Technologies (CVEST)
Institute	International Institute of Information Technology Hyderabad

---
/n frequency divider
Conventional Domino Logic
Reference-Design of Manchester Carry Chain Adder using
High speed Domino Logic

---
High Speed Domino Logic
Reference-Design of Manchester Carry Chain Adder using
High speed Domino Logic

---
Carry Generate Circuit
Reference-Design of Manchester Carry Chain Adder using
High speed Domino Logic

---
Carry Propogate Circuit
Reference-Design of Manchester Carry Chain Adder using
High speed Domino Logic

---
Manchester Carry Chain 1-bit Adder
Reference-Design of Manchester Carry Chain Adder using
High speed Domino Logic

---
Proposed Hybrid Adder in Paper
Uses 2 CLA and smaller CLA circuit to produce C8 for second 8-bit Carry-select adder
By that time Carry select adder has already done computation and output is
selected based on C8
Reference-A 16-bit High-Speed Low-Power Hybrid Adder

---
4-bit Manchester Carry Chain Adder
Used as 4-bit Carry Save Adder
Output calculated for both values of Cin and chosen with multiplexer based on
Carry provided by Carry Look-ahead Circuit
Reference-A 16-bit High-Speed Low-Power Hybrid Adder

---
Carry Look-ahead formulas
Reference-A 16-bit High-Speed Low-Power Hybrid Adder

---
Manchester Carry Chain Carry Look-ahead Circuit
Reference-A 16-bit High-Speed Low-Power Hybrid Adder

---
Flip-Flop-Cadence
Reference-A Partially Static High Frequency 18T Hybrid Topological Flip-Flop Design
for Low Power Application

---
Flip Flop-Cadence
Clock Frequency=250MHz

---
Thanks

---
Backup Slides